## Slide 1: Course - DT228/1 and DT282/1
Subject - Computer Architecture and Technology
FROM BOOLEAN ALGEBRA TO LOGIC GATES
Semester 2, Week 5

## Slide 2: The Algebra of Logic
Boolean algebra, sometimes referred to as the algebra of logic, is a two-valued system of algebra that represents logical relationships and operations.
Historically, the principle of two-value algebra began with the Greek philosopher Aristotle’s bivalent (two-mode) definition of truth with four foundational laws of logic.

## Slide 3: The Algebra of Logic (2)
Aristotle’s laws of two-value logic:
  The Law of Identity (A is A),
  The Law of Non-Contradiction (A is not non-A),
  The Law of the Excluded Middle (either A or non-A)
  The Law of Rational Inference.
  These so-called Laws function within the scope of logic where a proposition is limited to one of two possible values.

## Slide 4: George Boole
George Boole was a teacher and mathematician who lived between 1815 and 1864 – mostly in Lincoln, England. (He lectured in Cork for a few years when the university was called Queen’s College.)
Boole applied algebraic techniques to the logic processes for two-value systems.
He contended that any logical statement could be assigned a binary value, such as "true/false" or "yes/no."

## Slide 5: George Boole (2)
Boole discussed ways of reducing logical relationships to simple statements of equality, inequality, inclusion, and exclusion.
He then showed ways to express these statements symbolically using a binary (two-valued) code.
George Boole – 2 November 1815 - 8 December 1864

## Slide 6: George Boole (3)
He stated the algebraic rules that governed these logical relationships. This system of mathematical logic came to be known as Boolean algebra.
The algebra is based on one or two variables with logic of AND, OR and NOT applied to them as combinations of inputs.

## Slide 7: George Boole (4)
AND
  A (False) AND B (False) -> False
  A (True) AND B (False) -> False
  A (False) AND B (True) -> False
  A (True) AND B (True) -> True

## Slide 8: George Boole (5)
OR
  A (False) OR B (False) -> False
  A (True) OR B (False) -> True
  A (False) OR B (True) -> True
  A (True) OR B (True) -> True

## Slide 9: George Boole (6)
NOT
  A (False) -> True
  A (True) -> False

## Slide 10: Claude Shannon Takes Boole’s Algebra
In the 1930s, a graduate student of Massachusetts Institute of Technology called Claude Shannon described the Boolean type of algebra as matching the effects of switch and relay-switching circuits, therefore effecting bi-state or bipolar machinery…. 1s and 0s…. Digital things!
(John Von Neumann used these principles in his architecture… more on that soon.)

## Slide 11: Claude Shannon (2)
A (False) AND B (False) -> False
A (True) AND B (False) -> False
A (False) AND B (True) -> False
A (True) AND B (True) -> True
A (False) OR B (False) -> False
A (True) OR B (False) -> True
A (False) OR B (True) -> True
A (True) OR B (True) -> True
A (False) -> True (NOT A)
A (True) -> False (NOT A)
0 · 0 = 0
1 · 0 = 0
0 · 1 = 0
1 · 1 = 1
0 + 0 = 0
1 + 0 = 1
0 + 1 = 1
1 + 1 = 1
0 = 1
1 = 0

## Slide 12: Using Boolean Algebra with Binary
The basic principle of Boolean algebra is that a logic variable ‘X’ can have only one of two possible values or states:
X = TRUE or X = FALSE
In binary notation, we can say:
    X = TRUE = 1
X = FALSE = 0
This is called positive logic or high-true logic.

## Slide 13: Using Boolean Algebra with Binary (2)
We might also say:
X = TRUE = 0
X = FALSE = 1
This is called negative logic or low-true logic.
Usually the positive logic convention is used.

## Slide 14: Using Boolean Algebra with Binary (3)
Electrically, 1 is represented by a more positive voltage than zero and 0 is represented by zero volts.
Very often, on a microprocessor;
    x = TRUE = 1 = 0.5 volts (variable up to 0.8)
x = FALSE = 0 = 0 volts (or a small bit over 0)

## Slide 15: Boolean Arithmetic
With two states for input and output, it turns out that:
  Addition WILL work,
  Subtraction WILL NOT work,
  Multiplication WILL work,
  Division WILL NOT work.
  N.B. See Two’s Complement from Week 4’s notes.

## Slide 16: Boolean Arithmetic (2)
Addition works as OR:
    0 + 0 = 0
    0 + 1 = 1
    1 + 0 = 1
    1 + 1 = 1
1 + 1 can not be 0 – nor can it be 2, so Boolean logic means it has to be 1.

## Slide 17: Boolean Arithmetic (3)
Multiplication works as AND:
    0 x 0 = 0
    0 x 1 = 0
    1 x 0 = 0
    1 x 1 = 1

## Slide 18: Boolean Arithmetic (4)
A + B reads, A OR B,
A x B reads A AND B but since, in mathematics, generally, a dot (•) is used to show multiplication – or nothing at all – the notation of A•B or AB might appear for A AND B.

## Slide 19: Boolean Arithmetic (5)
NOT:
  The outputs in Boolean algebra can be affected by using NOT in the logic – i.e. you can invert inputs, A or B or the output, X by placing a NOT with the input before applying OR or AND, or just after the operation (OR or AND), thereby inverting the output.

## Slide 20: Boolean Arithmetic (6)
  The notation for NOT is a bar, a bubble or a ‘complement apostrophe’.
  So, for example, if A = 0 then NOT A = 1 and it might appear as either:
  Ā = 1
  Å = 1
  A’ = 1

## Slide 21: Boolean Arithmetic (7) Truth Tables
A | B |  | X
0 | 0 |  | 0
0 | 1 |  | 1
1 | 0 |  | 1
1 | 1 |  | 1
A | B |  | X
0 | 0 |  | 0
0 | 1 |  | 0
1 | 0 |  | 0
1 | 1 |  | 1
The OR Truth Table
The NOT Truth Table
The AND Truth Table
A |  | X
0 |  | 1
1 |  | 0

## Slide 22: Diagram of the Main Gates
Please note that an 'inverting buffer' is referred to and used to represent a NOT gate.

## Slide 23: The Principles of Logic Gates
The binary language used in today's computers reflects Boole's binary logic.
Modern computers operate solely on the binary numbers "1" and "0."
All the instructions that direct a computer's operation exist as a sequence of such binary digits or bits (0s and 1s).

## Slide 24: The Principles of Logic Gates (2)
Binary digits (or logical variables) are processed in the machine as distinct voltage states in tiny electronic circuits known as logic gates.
A logic gate only recognizes two varieties of input, high-voltage (value of 1 or TRUE) and low-voltage (value of 0 or FALSE).

## Slide 25: The Principles of Logic Gates (3)
The truth variables of Boolean algebra use the functionality of the logical concepts of AND, OR and NOT.
It will come as no surprise, therefore, that the logic gates (as electronic mechanisms) are AND, OR, and NOT.
These gates, used in differing combinations, allow the computer to execute all its operations and/or store its data.

## Slide 26: The Principles of Logic Gates (4)
Each logic gate of the types AND and OR takes in two or more bits in the form of such voltages, combines them according to a built-in rule, and produces a single high-voltage or low-voltage logical conclusion (output).
Note, though, that NOT gates usually have one input and one output.

## Slide 27: Digital Logic
Let A and B denote two propositions. (Here, propositions = declarative sentences that are either true or false but not both true and false at the same time).
If each proposition A and B is associated with a switch that will be closed if the proposition is "true" and open if the proposition is "false" then:
  the combined proposition AB (A AND B) may be instantiated by connecting the switches in series.
  Thus the output of one switch is the input of the other. Current can flow through the combined circuit if and only if both switches are closed, that is, if both A and B are "true."

## Slide 28: Gate Representations - AND

## Slide 29: Digital Logic (2)
  the combined proposition A + B (A OR B) may be instantiated by connecting the switches in parallel.
  Thus, with the switches side by side - so that both contribute to the output simultaneously – they can be used to represent the statement, A + B (A OR B). In this case current will flow if either switch is closed or if both switches are closed. That is, if A or B or both are "true."

## Slide 30: Gate Representations - OR

## Slide 31: Gate Representations – OR (2)

## Slide 32: Gate Representations - NOT

## Slide 33: Inside an AND Gate with Truth Table
A | B |  | X
0 | 0 |  | 0
0 | 1 |  | 0
1 | 0 |  | 0
1 | 1 |  | 1

## Slide 34: Inside an OR Gate with Truth Table
A | B |  | X
0 | 0 |  | 0
0 | 1 |  | 1
1 | 0 |  | 1
1 | 1 |  | 1

## Slide 35: Inside a NOT Gate with Truth Table
A |  | X
0 |  | 1
1 |  | 0

## Slide 36: Logic Gates for Data Movement
Logic gates are the fundamental building blocks of all digital logic circuits – they are switching circuits that perform certain simple operations on binary signals.
These operations are chosen to facilitate the implementation of functions such as changing 1s to 0s or 0s to 1, filtering 1s only or 0s only, checking for combinations of 1s and/or 0s.

## Slide 37: Logic Gates for Data Movement (2)
Why? Why are these filterings and conversions important to computer circuits?
That's the question I asked myself when I first saw logic gates. The reason: these allow for bits and bytes to be shifted through circuits and/or converted in the CPU.
Those shifts and conversions are the fundamental elements of computation. All action associated with components like the BIOS and the CPU need to use logic and algebra.

## Slide 38: NAND and NOR Gates
On (in) a silicone chip it is simpler to manufacture the combination NOT AND and NOT OR than it is to deal with AND, OR and NOT.
NOT AND becomes NAND.
NOT OR becomes NOR.

## Slide 39: NAND
The NAND gate looks like an AND gate with a ‘NOT bubble’ right on its output.

## Slide 40: The NAND Truth Table
The NAND Gate notation:
A NAND B = X
or
_____
A ● B = X
This reads as,
“A and B Bar equals X.”
A | B |  | X
0 | 0 |  | 1
0 | 1 |  | 1
1 | 0 |  | 1
1 | 1 |  | 0

## Slide 41: NOR
The NOR gate looks like an OR gate with a ‘NOT bubble’ on its output.

## Slide 42: The NOR Truth Table
The NOR Gate notation:
A NOR B = X
or
_____
A + B = X
This reads as,
“A or B Bar equals X.”
A | B |  | X
0 | 0 |  | 1
0 | 1 |  | 0
1 | 0 |  | 0
1 | 1 |  | 0

## Slide 43: The EXCLUSIVE OR Truth Table
A | B |  | X
0 | 0 |  | 0
0 | 1 |  | 1
1 | 0 |  | 1
1 | 1 |  | 0
The Exclusive OR Gate notation:
A XOR B = X
or
A B = X
This reads as,
“A x-or B equals X.”

## Slide 44: De Morgan’s Theorem
The mathematician, De Morgan had a theorem that showed that one gate could be made to work like another by inverting inputs and outputs.
There are two parts to the theorem:
Augustus De Morgan - 27 June 1806 - 18 March 1871

## Slide 45
The complement of two or more variables ANDed is equivalent to the OR of the complements of the individual variables.
___ __ __
(A ● B) = A + B
(NOT A AND B = NOT A OR NOT B)

## Slide 46
The complement of two or more variables ORed together is equivalent to the AND of the complements of the individual variables.
____ __ __
(A+B) = A ● B
(NOT A OR B = NOT A AND NOT B)

## Slide 47: More on DeMorgan’s Theorem
0 | 0 | 0 | 1
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 0
0 | 0 | 1 | 1 | 1
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 1
1 | 1 | 0 | 0 | 0
Proof
The truth-tables are equal; therefore, the Boolean equations must be equal.
Notes: Overview & proof of DeMorgan’s Theorem #1

## Slide 48: More on DeMorgan’s Theorem (2)
0 | 0 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 1 | 0
0 | 0 | 1 | 1 | 1
0 | 1 | 1 | 0 | 0
1 | 0 | 0 | 1 | 0
1 | 1 | 0 | 0 | 0
Proof
The truth-tables are equal; therefore, the Boolean equations must be equal.
Notes: Overview & proof of DeMorgan’s Theorem #2

## Slide 49: A Comparison Between Boolean and DeMorgan’s Theorems
Commutative Law
Associative Law
Distributive Law
Consensus Theorem
DeMorgan’s
Notes: Updates of the Boolean Theorems with the addition of DeMorgan’s

## Slide 50: The Theorem in Gates (Again)

## Slide 51: NAND and NOR Gates on CMOS
NAND and NOR gates are most commonly etched on the die of a CMOS chip
  (CMOS - complementary metal-oxide semiconductor, the architecture of most computer CPUs and memory modules.)
Why?
(Intel)
A
B
A
B

## Slide 52: NAND and NOR Gates on CMOS (2)
It is easier to implement groups of NAND and NOR gates on a chip than the AND, OR and NOT gates individually. (Overall, using NAND and NOR causes fewer inputs (a lower gate input count).
Also, they give a convenient conceptual representation.
(Intel)
A
B
A
B

## Slide 53: NAND and NOR Gates on CMOS (3)
The NAND gate is the natural implementation for CMOS technology in terms of chip area and speed.
The NAND gate is a universal gate: a gate type that can implement any Boolean function:
  NOT can be implemented with NAND
  AND implemented with the NAND gate
  OR using NAND (as in De Morgan’s Theorem)

## Slide 54: NAND and NOR Gates on CMOS (4)
Similar to the NAND gate, the NOR gate is a universal gate.
With a NOR gate you can implement:
  a NOT
  an AND
  an OR

## Slide 55: Next…
Next week we can take a look at sequential logic – an extension of the topics of Boolean algebra and logic gates.