## Slide 1: Course - DT228/1 and DT282/1
Subject - Computer Architecture and Technology
VON NEUMANN ARCHITECTURE - Part 1
Semester 2, Week 7

## Slide 2: John von Neumann
“The father of the modern computer.”
This quote is often cited in relation to John von Neumann.
Born in Hungary and named Neumann János Lajos Margittai, John spent a lot of time as a professor at Princeton University, USA.
A lot of his work was questionable (atomic bomb development) but he was a scientific genius. (Physics, mathematics, chemistry…)

## Slide 3: John von Neumann (2)
Mauchly and Eckert (as mentioned in the notes of Week 3) had mastered the architecture advances for which von Neumann has become famous while developing the ENIAC computer.
Von Neumann worked with Mauchly and Eckert and helped with the ENIAC project – but it was his publication of a journal paper on the internal workings of an ENIAC-type machine (called ‘First Draft’) that earned him the accolades.

## Slide 4: The Architecture
Before the ENIAC (Electronic Numerical Integrator And Computer) the electrical computing machines were manually loaded with instructions that were executed as they came through the processor – causing immediate output.
Von Neumann Architecture is based on ‘the stored program concept’.
Going from ‘in-the-moment’ computing to stored programs was a big leap in computing, at the time (mid-1940s).

## Slide 5: The Architecture (2)
The von Neumann Architecture is a computer design model that uses a single storage structure to hold both instructions and data.
A computer which implements the ‘referential model’ of specifying sequential architectures, in contrast with parallel architectures is described as having von Neumann Architecture.
The separation of storage from the processing unit is implicit in the von Neumann Architecture.

## Slide 6: Referential Model
The architecture developed by von Neumann, Mauchly and Eckert (as above), and the ‘stored program concept’ are the basis of the Referential Model.

## Slide 7: The Architecture (3)
The term ‘stored-program computer’ is generally used to mean a computer of this design.
Von Neumann begins his idea with a broad description of the general-purpose computing machine containing four main sub-components.
The sub-components relate to memory, control, central processing and connection with the human operator (sometimes defined as input/output).
These are represented by the arithmetic logic unit, the control unit, the memory, and the input-output devices of the classical computer model.

## Slide 8: The Architecture (4)
Diagram of the Architecture:

## Slide 9: The Architecture (4)
Another diagram of the Architecture – this matches the ENIAC architecture:
Main
Memory
Arithmetic
Logic Unit
Program
Control Unit
I/O
Equipment

## Slide 10: The Architecture (5)
In a special purpose machine the computational procedure could be part of the hardware. In a general purpose one the instructions must be as changeable as the numbers they acted upon.
To von Neumann the key to building a general purpose computing machine was in its ability to store not only its data and the intermediate results of computation, but also to store the instructions, or orders that allowed the computation.

## Slide 11: The Architecture (6)
Therefore, why not encode the instructions into numeric form and store instructions and data in the same memory?
This frequently is viewed as the principal contribution provided by von Neumann's insight (and Mauchly and Eckert’s) into the nature of what a computer should be.

## Slide 12: The Architecture (7)
The stored program concept was proposed about sixty years ago – and it is the fundamental architecture employed by computers.
Computer technologies come and go (or get superceded) but the stored-program concept endures.

## Slide 13: The Stored Program Concept
The stored program concept had several technical implications:
  Four key sub-components operate together to make the stored program concept work.
  The process that moves information through the sub-components is called the ‘Fetch-Execute Cycle’.
  Unless otherwise indicated, program instructions are executed in sequential order.

## Slide 14: The Four Sub-Components
Physically, the four sub-components in von Neumann Architecture might be called:
  Input/Output (or ‘I/O’)
  Control Unit
  Arithmetic-Logic Unit
  Memory
While only four sub-components are listed in the books, there is a fifth part to the operation: a bus (or wire) that connects the components together and over which data flows from one sub-component to another. (More on buses next week.)

## Slide 15: Memory
There are several different types of memory at processor level:
  RAM (Random Access Memory)
  ROM (Read Only Memory)
  Registers
  Cache
Why not just engineer one type?
Each type of memory represents cost/benefit tradeoffs between capability and cost …

## Slide 16: Memory (2)

## Slide 17: Memory Types
RAM is an array of cells, each with a unique address.
It should take the same amount of time to access any memory cell, regardless of its location with the memory bank. (‘Random’ access.)
ROM memory cells can be read from, but not written to. Cells are protected.
ROM is more expensive than RAM and only critical information is stored. (I.e. Firmware instructions.)

## Slide 18: Memory Types (2)
Register cells are powerful, costly, and physically located close to the heart of computing.
Some registers are the main participants in the Fetch-Execute Cycle. (More on the Fetch-Execute Cycle later.)
Cache memory is a type of RAM. The main difference between cache and actual RAM is that cache is addressed by the CPU before RAM - so instructions may be performed quicker if in cache.

## Slide 19: Memory Addressing
For all these memory types, cell size or cell width is a measure of how many individual memory cells (switches for bits) are addressed at a time.
At a minimum, this is a byte (8 bits) but to support all data types and operations cell size can be larger (example, a word of 16 bits).

## Slide 20: Memory Addressing (2)
https://www.youtube.com/watch?v=bTj0vFs8ndI

## Slide 21: Memory Addressing (3)
All cells have an address and can contain data (where data = data or instructions).
The cell address is a label (like a post code) that identifies a particular cell.
The cell contents are whatever data is stored at a given address location.

## Slide 22: Memory Addressing (4)
The memory labels are themselves binary numbers.
One of the internal registers is used to hold address locations. (MAR – memory address register or machine address register.)
This register has to be big enough to hold the biggest address of a memory location.

## Slide 23: I/O: Input and Output
There is both a human-machine interface and a machine-machine interface to I/O.
Examples of the human-machine interface include a keyboard, screen or printer.
Examples of the machine-machine interface include things like mass storage and secondary storage devices.

## Slide 24: Arithmetic Logic Unit - The ALU
The third component in the von Neumann Architecture is called the Arithmetic Logic Unit.
This is the subcomponent that performs the arithmetic and logic operations based on combinations of flip-flops, latches and gates, generally.
The ALU is the “brain” of the computer.

## Slide 25: The ALU (2)
The graphic on the left is a 3-D lego-type representation of the ALU

## Slide 26: The ALU (3)
The ALU contains many of the registers.
Its flip-flop and latch circuitry allows it to perform addition, subtraction, multiplication and division, as well as logical comparisons: less than, equal to and greater than.

## Slide 27: Control Unit
The control unit drives the fetch and execute cycle.
As mentioned before, in memory, a cell address is loaded into the MAR – it is the control unit that figures out which address is loaded, and what operation is to be performed with the data moved to the memory data register (or machine data register) - MDR.

## Slide 28: Control Unit (2)

## Slide 29: Control Unit (3)
To do its job, the Control Unit has several tools
  Special memory registers
  ‘Hard-wired’ understanding of an Instruction Set

## Slide 30: Control Unit (4)
Special Memory Registers
  The Control Unit must keep track of where it is within a program, and what it should do next
  Two special registers are used to accomplish this:
    A program counter, typically referred to as a PC, holds the address of the next instruction to be executed.
    An instruction register, typically referred to as an IR, holds an instruction fetched from memory.

## Slide 31: Control Unit (5)
Along with the special registers, the Control Unit utilises special circuitry, called an instruction decoder.
The instruction decoder is a typical decoder circuit, and its purpose is to read an instruction from the instruction register (IR), and then to activate the appropriate circuit line.

## Slide 32: How this Works
Remember, we are trying to figure out how the stored program concept works.
In this model, the program and the data upon which it operates are stored in memory locations.
We know how to encode the data.
We need to learn how to encode the programming instructions.

## Slide 33: The Instruction Set
At the heart of all programming are a few basic, general instructions.
The set of instructions is small and particular to the processor’s specification.
The power of the instruction set is that by identifying a definite, bounded, simple task, an instruction can be executed with appreciable speed (typically within a few billionths of a second).

## Slide 34: The Instruction Set (2)

## Slide 35: The Instruction Set (3)
The instruction set is something like the ASCII alphabet encoding scheme.
The specific instructions are given unique binary codes.
Obviously, the instruction register must be big enough to hold any instruction within the numbered set.

## Slide 36: Execution Happens in Cycles
Data and program instructions are translated into binary form and stored in RAM.
As the information is needed, it is moved to the high speed, costlier registers where it is processed.
This process occurs in a cycle: fetch information to the registers, and execute it there, fetch the next information from the registers, and execute it, etcetera.

## Slide 37: Engineering Needs
Once we know on which data we should be working, we know how to build circuitry to perform processing operations. (We can add, subtract, divide and compare).
How do we figure out what data to be working on, and exactly which operation to perform?

## Slide 38: Engineering Needs (2)
Specifically, this is what we need to be able to do:
  Build a circuit that will allow us to take whatever number is in the Memory Address Register (MAR), and use this number to access a specific memory cell.
  Build a circuit that will allow us to choose which data results should be placed in the Memory Data Register (MDR).
This magic happens in the Control Unit (also known as the PCU (Program Control Unit)

## Slide 39: Choosing a Memory Location
The initial requirement first: how do we determine which address location holds the data on which we need to operate?
As mentioned before, the MAR holds an address - a binary number.
We need some circuitry to read that number, and based on its value, find exactly the correct address location to read.
The circuit is called a decoder …

## Slide 40: Decoder

## Slide 41: A Von Neumann Architecture Effect
The idea of the ‘stored program concept’ had a specific effect: The stored program needed to have procedures to allow the individual instructions and data to be ‘called and dealt with’ – a fetch and execute arrangement (or fetch-execute-store arrangement).

## Slide 42: The Fetch-Execute Cycle
The CPU executes a program that is stored as a sequence of machine language instructions in main memory.
It does this by repeatedly reading, or fetching, an instruction from memory and then carrying out, or executing, that instruction.

## Slide 43: The Fetch-Execute Cycle (2)
This process of ‘fetch an instruction, execute it, fetch another instruction, execute it and so on’, is called the Fetch-Execute Cycle.
This continuous check that the CPU makes; fetching, executing and pushing out the result, is called ‘polling’ but can be interrupted by an ‘interrupt’.

## Slide 44: The Fetch-Execute Cycle (3)
This is a two-cycle process because both instructions and data are in memory.
Fetch
  Decode or find an instruction, load from memory into a register and signal the ALU.
Execute
  This performs an operation that the instruction requires.
  Move/transform data.

## Slide 45: The Fetch-Execute Cycle (4)

## Slide 46: The Fetch-Execute Cycle (5)
With an interrupt the CPU reacts to a signal to ‘jump’ to an address. There will be ‘interrupt handler’ instructions there.
An interrupt handler is part of the device driver software for the device that signalled the interrupt.
It will allow the diversion to another program and, after the interrupt, direct the CPU back to the previous program – ‘where it left off…’

## Slide 47: The Fetch-Execute Cycle (6)
Instruction cycle example:
  The ALU and PCU are used for the fetch-execute cycle:
  Arithmetic and Logic Unit - ALU
  The ALU is part of the Central Processing Unit. All computations are performed in this unit.
  The ALU comprises adders, counters, and registers, numerical operations (+ - / x) and logical operations (AND, OR, program branching).

## Slide 48: The Fetch-Execute Cycle (7)
  (Program) Control Unit - PCU
  The PCU :
    Coordinates all other units in the computer,
    Organises movement of data from/to Input/Output, memory and registers.
    Directs ALU, specifically to indicate the operations to be performed.
The control unit operates according to the stored program, receiving and executing its instructions one at a time.

## Slide 49: The Fetch-Execute Cycle (8)
Instruction Cycle (or Fetch-Execute Cycle)
Fetch Cycle;
Fetch instruction from memory
Execute Cycle;
Decode instruction,
Fetch required operands,
Perform operation.

## Slide 50: The Fetch-Execute Cycle (9)
The components of a processor
  DR - Data Register
  M - Memory
  MAR – Memory Address Register
  MBR (or MDR) – Memory Buffer Register (or Mem Data Reg)
  AC - Accumulator
  PC - Program Counter
  IR - Instruction Register
  ALU - Arithmetic Logic Unit (including arithmetic logic circuits)
  PCU - Program Control Unit

## Slide 51: The General Sequence to a Fetch-Execute Cycle
A program, stored in the main memory of a computer, is ‘obeyed’ by the CPU carrying out the following sequence of events, described with the symbolic notation:
    1. [PC] -> MAR
    2. [M] -> MBR
    3. [PC]+1 -> PC
    4. [MBR] -> IR
    5. Decode
    6. Execute this instruction
    7. Repeat from step (1)

## Slide 52
START
Instruction awaiting execution?
Fetch next instruction
Execute next instruction
Interrupt requiring servicing?
Transfer control to interrupt-handling program
No
No
Yes
Yes
Fetch Cycle
Execute Cycle
Program Transfer

## Slide 53: Overview of the Fetch-Execute Cycle
RAM holds machine language programs and data.
The CPU fetches machine language instructions from Cache or RAM (but possibly a 32 bit register) one after another and executes them without understanding what it does or how it does it.
So the program it executes must be perfect, complete and unambiguous because the CPU can do nothing but execute instructions exactly as they are written.

## Slide 54: End of Part 1
That was the first of two lectures on the von Neumann Architecture.
Next week :
  Von Neumann Architecture, Part 2