## Slide 1: Course - DT228/1 and DT282/1
Subject - Computer Architecture and Technology
NETWORKS
Semester 2, Week 10

## Slide 2: What is a Computer Network?
In computer technology a computer network is a collection of independent computers that are connected together to exchange or share data and/or software.
Put another way, ’A network is a series of points or nodes interconnected by communication paths’.

## Slide 3: Node? What is a ‘node’?
Describing topology, we use the term node to refer to any independent component (device) of the network.
Those might be such things as the workstation or personal computer, server, printer…

## Slide 4: How Do Networks Exchange Data?
A computer network may be ‘fixed’ – i.e. connected permanently using cables - or their links might be temporary - as when connected via modems. Wireless networks generally work using waves in the air and are passed and then processed over ‘WiFi’ (Wireless Fidelity – a wireless local area network) or a proprietary carrier's networks – carriers being Eircom and ESAT BT.
(These variations will be expanded on later.)

## Slide 5: How Fast Can Networks Exchange Data?
Network transmission speeds, measured in bits per second, range from only a few thousand bits per second (Kbps) for old networks, to millions of bits per second (Mbps).
High-speed networks often operate at around 100-200 Mbps (in an office of 2 - 20 computers) and ‘special’ applications of technology offer billions of bits per second (Gbps) (in a laboratory environment, perhaps).

## Slide 6: Size (How big an area does a network cover?)
A local area network (LAN), using cable, covers a geographically limited area, generally contained within a single building, or a few physically-close buildings (with a building-to-building gap of about 25 metres) – but they may go to a square kilometre at a stretch.
Networks spread over a larger area – wide area networks (WAN) – often span regions such as a province, state, a whole country or among countries.

## Slide 7: Size (2)
Imagine these servers and stand-alone computers on different floors in two office blocks that are within 25 metres, say.

## Slide 8: Common LAN Topologies
Four common Local Area Network topologies exist: bus, ring, star, and tree. (Five, if you include the ‘hybrid’ topology.)
These topologies are logical architectures, but the hardware devices need not be physically organised in these configurations. Logical bus and ring topologies, for example, are commonly organised physically as a star.

## Slide 9: Common LAN Topologies (Bus)
A Bus Topology

## Slide 10: Common LAN Topologies (Star)
A Star Topology

## Slide 11: Common LAN Topologies (Ring)
A Ring Topology
Terminal
Computer
Terminal
Terminal
Computer
Printer

## Slide 12: Common LAN Topologies (Tree)
A Tree Topology
A Tree Topology

## Slide 13: Network Switching
To control the data traffic on a computer network the method of switching is used. There are two main switching methods for networks:
  Packet switching
  Circuit switching

## Slide 14: Network Switching (2)
Packet-switched - a type of network in which relatively small units of data called packets are routed on a network with a destination address contained within each packet.
Circuit-switched - a type of network where a physical path is obtained for and dedicated to a single connection between two end-points in the network for the duration of the connection. Example: a telephone network.

## Slide 15: The Network Router
In packet-switched networks a router is a device (and/or software) in a computer that determines the next network point to which a packet should be forwarded to take it closer to its destination. The router is connected to at least two networks and decides which way to send each information packet based on the state of the networks it is connected to. A router is located at a gateway - the hardware point where one network meets another.

## Slide 16: The Network Router (2)
Wireless router hardware
Cisco routers (as might be used in an office or lab)

## Slide 17: The Network Router (3)
A router is often included as part of a network switch.
Router software may create or maintain a table of available routes and their conditions. The program will use this information along with distance and cost algorithms to determine the best route for a given packet.
Routing is a function called ‘Layer 3’ - it is part of a standard for engineering networks - a model called Open Systems Interconnect(ion) (OSI).

## Slide 18: Client Server Networks
Client Server, client-server, client/server…
Client-Server describes the relationship between two computer programs where one program, the client, makes a service request from another program, the server, which fulfills the request.
Although the client-server idea can be used by programs within a single computer, it is more often associated with networks.

## Slide 19: Client Server Networks (2)
Client Server networks:
A client/server system includes one or more servers to store programs and/or data in a central location.
Users (clients) access the programs or data when their software request to the server, across the network, is dealt with.
The client-server model provides a convenient way to interconnect programs and data that are distributed efficiently across different locations.

## Slide 20: Client Server Networks (3)
Star Type
Bus Type

## Slide 21: Client Server Network Example
The best known recent client/server application is the World Wide Web – the Internet.
Users send requests for a specific web page and the page is transmitted from the server to the client for display on the client's screen.

## Slide 22: Client Server Network Example (2)
This puts the web page database activities on the server where the web pages are stored but puts the graphics processing needed to display the page on the local machine where the request originated.
The request/reply protocol for these exchanges is called Hypertext Transfer Protocol and is commonly known as HTTP.

## Slide 23: Software for Networks – Communication Software
Computers that are connected need communication software to interact. This software will control the flow of data from node to node.
The signals, messages and files that move from one node (computer, server…) and another need to be managed. That includes checking the format of the signal, message or file.

## Slide 24: Network Operating System
The software used to control many of these elements is in the form of a ‘network operating system’.
There are many forms for a network operating system (NOS).
An example of a NOS is Novell NetWare (albeit an older and soon-to-be obsolete NOS).

## Slide 25: NetWare
NetWare, made by the company known as Novell, was probably the most widely-installed network server operating system.
Initially NetWare was successful in large and small office local area networks, Novell has redesigned (or refeatured) NetWare to work successfully as part of larger and heterogeneous networks, including the Internet.

## Slide 26: NetWare (2)
Up until the mid-2000s NetWare was strongly affiliated to the Unix and Linux operating systems: NetWare 6 associated with Unix work, NetWare OES (Open Enterprise Server) associated with Linux.
Novell suffered from management problems and were bought out by the ‘Attachmate’ company.
Microsoft’s Network Operating Systems became popular instead.

## Slide 27: Protocol
To communicate with each other, two machines must follow the same protocol.
A protocol is the special set of rules that end-points in a telecommunication connection, such as two PCs on a Local Area Network, use when they communicate. They are, essentially, a type of system software.

## Slide 28: Protocol (2)
A protocol includes formatting rules that specify how data is packaged into messages.
It also may include conventions like message acknowledgement or data compression to support reliable and/or high-performance network communication. (In other words, it makes sure the data on high-speed communications are received ‘loud and clear’…)

## Slide 29: Protocol (3)
Protocols include prearranged 'messages' between computers that establish, for example, whether a receiving machine is ready, whether a file was received properly….
Both end points must recognise and observe a protocol so that the binary signal format of a transmission will be recognised and accepted by the receiving device. Protocols are often described in an industry or international standard.

## Slide 30: Protocol (4)
Looking at a typical protocol as a file transfer and management tool one might see these features:
  File group transmission,
  File attribute transmission (size, date, permissions, etc)
  File name, record-format, and character-set conversion,
  File collision options,
  /continued…

## Slide 31
  File transfer recovery,
  Auto upload and download (of data or files)
  Client/Server operations,
  Automatic per-file text/binary mode switching,
  Recursive directory-tree transfer,
  Uniform services on serial and network connections,
  An Internet service daemon.

## Slide 32: Daemon?
A daemon (pronounced dee-muhn) is a program that runs continuously and exists for the purpose of handling periodic service requests that a computer system expects to receive. The daemon program forwards the requests to other programs (or processes) as appropriate. Each server of pages on the Web has an HTTPD or Hypertext Transfer Protocol daemon that continually waits for requests to come in from Web clients and their users.

## Slide 33: Daemon (2)
The daemon program that runs in the background (as a systems software program does), rather than under the direct control of a user.
Typically, in Unix, daemons have names that end with the letter ‘d’; for example, ‘syslogd’ is the daemon which handles the system log.

## Slide 34: Protocols – A Visual
I will try to get this list of acronyms as references in the tutorial

## Slide 35: More on Protocols
There are usually seven layers to many network communications – in terms of protocols:
    Physical layer
    Data link layer
    Network layer
    Transport layer
    Session layer
    Presentation layer
    Application layer

## Slide 36: More on Protocols (2)
To start with, at the physical layer, at the lowest level, bits are encoded in electrical, signals, light or radio signals.
At the data link layer errors might be detected. The transmission system has to be configured at this point.
The network layer deals with addressing for the transmission.

## Slide 37: More on Protocols (3)
The transport layer deals with error detection and retransmission in the case of a faulty transmission.
The session layer responds to service requests from the presentation layer and issues service requests to the transport layer.
The presentation layer responds to service requests from the application layer and issues service requests to the session layer.

## Slide 38: More on Protocols (4)
The application layer interfaces directly a user’s network applications.
It performs application services for the application processes such as handling requests for data from a remote node.
So this is the level where the user runs network functions – an example might be to ‘click on a link’ on the Internet.

## Slide 39: More on Protocols (5)
Internet protocol
On the Internet, there are the TCP/IP protocols, consisting of:
  Transmission Control Protocol (TCP), which uses a set of rules to exchange messages with other Internet points where 'information packets' are being sent.
  /continued…

## Slide 40
  Using TCP, applications on networked host machines can create connections to one another to exchange data or packets.
  This protocol is known as being reliable in delivering sender-to-receiver data.
  TCP also distinguishes data for multiple applications happening at the same time
/continued…

## Slide 41
  Internet Protocol (IP), which uses a set of rules to send and receive messages at the Internet address level.
  IP is a data-oriented protocol used for communicating data across a packet-switched internetwork... (That will be the Internet, then? Aye.)
/continued…

## Slide 42
  Additional protocols that are usually included with TCP/IP are the Hypertext Transfer Protocol (HTTP) and File Transfer Protocol (FTP), each with defined sets of rules to use with corresponding programs that appear on the Internet in different places but need to be run to allow files to be sent/received.

## Slide 43: Hardware for Networks – Network Transmission Media
Network transmission media generally fall into one of the following groups:
  Copper wire - carries electrical signals, much like telephone or cable TV wiring.
  Optical fibre - carries light-waves, either from lasers or Light Emitting Diodes.
  Wireless - radio signals or infra-red light pulses
Each medium has its own advantages and disadvantages .

## Slide 44: Copper Cable
Copper wire for network data transmission comes in two forms:
  twisted-pair cable,
    Similar to telephone cables, that contain 2 or more parallel wires that are twisted around each other, and
  coaxial cable,
    Similar to the cables used for cable TV. Each type of cable uses a different type of connector to interconnect computers or other hardware on the network.

## Slide 45: Unshielded Twisted Pair Cable
Twisted pair cable comes in two varieties: shielded and unshielded. Unshielded twisted pair (UTP) is the most popular and is generally the best option for LAN networks.
        Fig. 1. Unshielded twisted pair
The quality of UTP may vary from telephone-grade wire to extremely high-speed cable.

## Slide 46: Unshielded Twisted Pair Connector
RJ-45 is the standard for unshielded twisted pair cabling connector. This is a plastic connector that looks like a large telephone-style connector. A slot allows the RJ-45 to be inserted only one way. RJ stands for Registered Jack, a kind of standard. This standard designates which wire goes with each pin inside the connector.
Fig. 2. RJ-45 connector

## Slide 47: Shielded Twisted Pair Cable
A disadvantage of UTP is that it may be susceptible to radio and electrical frequency interference. Shielding reduces or removes these effects.
The shield acts as an ‘earthing’ or ‘ground’ in circuitry terms.
Fig. 3. Shielded twisted pair

## Slide 48: Coaxial Cable
Coaxial cabling has a single copper conductor at its centre, a plastic layer provides insulation between the centre conductor and a braided metal shield. The metal shield helps to block any outside interference from fluorescent lights, motors and other computers.
Fig. 4. Coaxial cable

## Slide 49: Coaxial Cable Connector
Bayone-Neill-Concelman (BNC) connector is sometimes used for coaxial cables. Connectors on the cable are the weakest points in any network. To help avoid problems with your network, the BNC connectors that crimp, rather than screw onto the cable are better.
Fig. 5. BNC connector

## Slide 50: Fibre Optic Cable
Fibre optic cables are not affected by electrical interference and can carry data both at far higher transfer rates and for much greater distances than any copper cables.
In the past, the higher cost of optical fibre restricted its use to high-interference locations and network backbones (trunk lines) but its cost has dropped significantly in recent years and it is being used for all but the shortest distances (where twisted-pair is more convenient).

## Slide 51: Fibre Optic Cable (2)
The major disadvantages of using optical fibre:
  It can be more difficult to install in older buildings because it cannot be bent around corners as sharply as copper wire.
  It is more difficult to attach connectors to optical fibre than to copper cable.

## Slide 52: Fibre Optic Cable (3)
Fibre optic cable is used when high speed networking is required. Example: live video feed through networked computers with high-specification graphics processing.
Fig. 6. Fibre optic cable

## Slide 53: Fibre Optic Cable (4)
Fibre optic cable consists of a centre glass core surrounded by several layers of protective materials, which enables it to transmit light signals at great speeds over much longer distances eliminating the problem of electrical interference.
Another example: optic cabling is ideal for environments that contain a large amount of electrical interference.

## Slide 54: Fibre Optic Cable (5)
Here is a better diagram of a fibre optic cable…

## Slide 55: Wireless Media
The range of transmission media for wireless networks is vast and still growing.
Originally, standard two-way radios were used, but they were very limited in reliability and transmission speed.
Point-to-point microwave radios, like those used by TV stations and telephone companies provide higher transfer rates (several Mbps) and are more reliable, but require tall towers and expensive hardware.

## Slide 56: Wireless Media (2)
For longer distances, satellite relays can deliver Kbps, but are very expensive to build and operate.
Within a building, infra-red light pulses, like a TV remote control uses, work well for short distances, but at low transmission rates.

## Slide 57: Point to Point Transmission of Microwave Radio Signals

## Slide 58: Point to Point Transmission of Microwave Radio Signals (2)

## Slide 59: Point to Point Transmission of Microwave Radio Signals (3)

## Slide 60: Internetworking
An internetwork is a collection of individual networks, connected by intermediate networking devices, that functions as a single large network. Internetworking refers to the industry, products, and procedures that meet the challenge of creating and administering internetworks. The diagram below illustrates some different kinds of network technologies that can be interconnected by routers and other networking devices to create an internetwork.

## Slide 61: Internetworking (2)
Different network technologies can be connected to create an Internetwork

## Slide 62: On an Internetwork
The more visible aspects to a user of ‘internet’ is the browser.
A browser is a graphical user interface-based hypertext client application, such as Explorer, Mosaic, and Netscape Navigator, used to access hypertext documents and other services located on remote servers throughout the WWW and Internet.
The visible language is ‘Hypertext’.

## Slide 63: Next…
Next time we can finish the notes by taking a look at new ideas in architecture and technology.
… in ‘New Architectures and Technology’.