## Slide 1: DT 228-1 and DT282-1 Computer Architecture and Technology
Tutorial 8

## Slide 2: Questions and Answers ( 1 )
What are interface types?
The interface types of the Week 9 lecture relate to PC (personal computer) interface types mostly, and their development over recent years.
These interfaces are electronic, they represent connections or ‘junctions’ (my term) for buses or cables that carry data, or data and electrical power.
They have many different appearances, physically.
They are usually parallel types or serial types.

## Slide 3: Questions and Answers ( 2 )
What are the main interface considerations?
Whether internally or externally, computer interfaces need to be constructed for efficiency and reliability (including data and power efficiency).
That construction needs design, and design is directly related to architecture – at ‘chip’ level, out to ‘cable’ and peripheral interface level. (The small out to the large).

## Slide 4: Questions and Answers ( 3 )
Why are there so many types?
The reason why there have been many types of interface is because the architectures for PCs and Apple (and now Android) have changed to meet new technologies and user demands.
The development history has been reactive to rapid change: the computer companies have responded with their own interface types - where some have endured and others have been replaced. (USB is a very interesting story – a company thriving on one very good idea.)

## Slide 5: Interface Types on Youtube
My pick of Youtube clips for hardware interfaces:
Serial ATA connectors – well explained
https://www.youtube.com/watch?v=TvZr8Pr3_vE
New USB cables – including USB 3 and USB C
https://www.youtube.com/watch?v=WDJWjqyjcwM
Display Interfaces Compared (HDMI, Displayport, DVI, Thunderbolt)
      https://www.youtube.com/watch?v=3LoGJZmyfpA

## Slide 6: Typical Exam (Sub) Question For This Content
Question
Describe the main architectural features of the ‘northbridge’ and ‘southbridge’ of a chipset.
Sample solution
The northbridge, also known as the Memory Controller Hub (MCH), is traditionally one of the two chips in the core logic chipset on a PC motherboard, the other being the southbridge. Separating the chipset into northbridge and southbridge is common, although there are rare instances where these two chips have been combined onto one die when design complexity and fabrication processes permit it.

## Slide 7: Solution continued
The northbridge connects to higher-speed devices than the southbridge.
The northbridge typically handles communications between the CPU, RAM, AGP or PCI Express, and the southbridge. Some northbridges also contain integrated video controllers, which are also known as a Graphics and Memory Controller Hub (GMCH). Because different processors and RAM require different signalling, a northbridge will typically work with only one or two classes of CPUs and generally only one type of RAM.
Buses and standards managed by southbridges (including USB, IDE, PCI, Audio, LAN, and Super I/O legacy devices).

## Slide 8: Solution continued
Connecting the southbridge: During the Pentium era chipset designers avoided bottlenecks in motherboard designs. As peripheral connections became more sophisticated it became obvious that the PCI bus could no longer be used to connect the north and southbridge chips.
The PCI was not efficient enough. Improvements in device speeds of internal and external devices created larger bandwidth requirements for the connection between north and southbridges.
(10 marks)